# Introduction

The framework is for those who are ready for the next step. Engineers, students and hackers that are ready to learn to program using real ANSI C, the language of the MCU. Recent surveys have indicated that ANSI “C” is the predominate language used in this domain. And for a good reason, it is a very efficient and a powerful weapon. It is really a substitute for assembly language and if used well it can end up being more efficient and has a high degree of portability.
Using the Firebird32 Family and Codewarrior from Freescale provides an unparallelled opportunity to learn MCUs inside out with a well supported, full symbolic debugger at a very low entry cost. A single click will flash the device and prepare the environment. As you single step through the code you can not only view all variables, but also the view the actual assembly language as well as all the registers.
While C++ offers some real advantages in other domains, it is really not for this type of development. For one thing, there is a certain amount of overhead to using real object oriented design. Also, to really leverage the power of C++, dynamic memory allocation is required, and this is generally not a good idea on a machine that has so little ram. I personally don't even use malloc.
Although the term “C/C++” is used quite often, be aware that these are really two different languages that only share a degree of syntax similarity.
Assuming are you are not an artist interested in flashing LEDS your goal is to have faultless code that never ever crashes and can run virtually indefinitely with out a fault. To do this requires careful consideration of how resources are being used (the main reason I don't use malloc), attention to detail and a fair amount of testing.
Like all powerful weapons, you are able to shoot your self in the foot, so if you are unfamiliar with “C”, as you proceed please take the time to really learn “C”. The internet is rich with information on this subject.
Many of the wiring framework functionality is derived from the standard “C” libraries and offers a richer selection than the standard wiring “language” does. Again, very well tested and document libraries.
## Why a Framework?
A framework provides an easy pre-tested path to getting your application up and running sooner. As with all frameworks, some compromises must be made to facilitate both ease of use and broad flexibility. Too flexible and it becomes difficult to configure and use. Not flexible enough and it will not have a broad application base.
This framework is loosely based on the Wiring/Processing library, but does not use and C++ at all. C++ introduces large penalties in storage and time and is generally not used in this type of application (“bare metal” hard realtime).
It is designed and tested with Freescales Eclipse based Code Warrior, which as of this writing is at version 10.1.
It is assumed in this document that reader has used the “C” programming language and no attempt is made in this document to explain the “C” language.
The framework is provided as “C” and “H” files, that are to be included in the Eclipse project, but not copied into the workspace. If you decide to modify the frameworks, be aware that this may cause a problem with future updates and merging. There follows a more detailed explanation of how this all works.
Some of the functionality is provided by the standard “C” libraries. For example “math.h” is used to provide trig functions and other math functions.
## Project Structure
This section explains the directory structure and components required to create a framework project from scratch. If you are using a provided sample project, you need not do any of this.
The projects relies on the files being in certain places and use relative paths so that the Framework directories are above workspaces. This makes it easy for several workspaces to use them.
As this framework is similar to the Wiring/Processing language, the functions loop() and setup() are used. The function setup() is called at the start of the program, and each time loop() returns it is called again. You are certainly not obliged to use this set up, but the examples are geared to this. I have found it is really quite convenient to use this structure.

There is also a third function I have added which must be defined, RTCTickCallback(), which is called at 1 millisecond intervals. This is quite handy for performing periodic tasks, but note that it is called in the context of an interrupt and there are do's and don'ts that should be followed. It must be understood that since it is called at 1 millisecond intervals, if the function took 1 millisecond to execute it would consume 100% of the cpu's time, and lock out other interrupts, 500us would take 50% and so on.

As will be mentioned later, it is important to understand that there are two basic way a file can be added to a project. They can be added using copy or as links. Some files should be added as links, like the framework proper files, as this way when you update the framework all you projects will see the new files. Other files, such as config.h, should be copied as if you modify it for the project, would not want to change the default one. Also if you are starting a project from a sample file, you would copy it as again you would be modifying it.

Another important thing to know that that if linked files are deleted from a project, only the link is deleted not the file. If a file that is in a project directory is deleted, the file is actually deleted. Files that are copied into a project directory are automatically added to the project.

After adding or removing a file from a project, the project must be cleaned and rebuilt, or you will get errors about the make file. When you clean the project, the makefiles are re-created.

Always Clean and Rebuild the project after adding or removing files or include paths!
### Directory Structure
The framework uses a certain directory structure:
--Project Directory ( e.g C:\CWProjects )
 |--- Framework (the framework files C:\CWProjects\Framework)
 |---Framework/Headers (C:/CWProjects/Framework/Headers)
 |---Framework/Sources (C:/CWProjects/Framework/Sources)
 |---Framework/Samples (C:/CWProjects/Framework/Samples)
 |---WORKSPACE
 |---ECLIPSE PROJECT DIRECTORY

Illustration 1.1: Directory Structure
### CONFIG.H and ALL.H
The file CONFIG.H must be in the projects Project_Headers folder, and should be added as a copied file. There are standard ones provided or it can be customized. Please see comments in the file as new features will be added.
ALL.H is an include file that includes all the other framework include files. It should be included in all source files that use the frameworks. The added include paths will find this file.
## I/O Channels
The Framework uses I/O channels for digital I/O, analog I/O and interrupts. The digital channels are configurable both internally and by the user. Analog and interrupt channels are predefined, and assigned to to the MCU pins that support there function. Since almost all MCU pins can also be digital I/O there is a flexible method of assignments of logical channel to digital MCU pins.
The assignments for digital I/O to physical MCU pins is accomplished using PIO (port i/o) tables.
### Digital Channels
The assignments for digital I/O to physical MCU pins is accomplished using PIO (pin i/o) tables. There are three predefined tables, for the Firebird32, the Nano32 and the Mini32. The term “pin” actually refers to a digital channel, which in turn maps to a MCU pin.
See the appendix for you board.

// NO NEED TO DO THIS FOR STANDARD BOARDS.
// For customizing only!!!!

BEGIN_PIO_TABLE(mytable)
PIO_ENTRY(D_PORTE,BIT2) // PTE1 TX
PIO_ENTRY(D_PORTE,BIT0) // PTE0 RX
PIO_ENTRY(D_PORTG,BIT3) // PTG3
PIO_ENTRY(D_PORTE,BIT2) // PTE2 TPM1CH0
END_PIO_TABLE(mytable)

 Then, to cause the framework to use this table:
setPIOTable(PIO_TABLE(mytable));
pinMode(0,OUTPUT); // Use the first channel in my table.
digitalWrite(0,1);

It is important to use these macro as it will insulate the code from future implementation changes in the internal pio table structure.
See Also Table PWM Channels and Table Interrupt Channels for a listing of these per-set channels.

### Analog Channels
The analog channels are pre-set to the analog channels supported in the MCU. There is no advantage to changing these. Please see the Table in chapter 2 in the description of the Analog Read API function.
The number of bits returned from an analog read can be configured in CONFIG.H, however the frame always reads 12 bits.

### PWM Channels
The PWM channels are preset to the MCU timer channels that support PWM. Please the read the description in the Analog Write API description.

## setup(), loop() and RTCTickCallback()

These three functions are the starting point for all applications. Below is the preferred method for blinking the LED, as delay() stalls loop() and prevents other perhaps critical code from running.

/*
 * loop_blink_fb32.c
 */

#include <hidef.h> /* for EnableInterrupts macro */
#include "derivative.h" /* include peripheral declarations */

// All.h includes all the include files for the framwork.
#include "ALL.H"

// Function Prototypes
void RTCTickCallback(void);
void setup(void);
void loop(void);

int counter = 0;	// Determine when 1/2 a second is up.
int blink_state=0;	// Toggles with XOR

// Called every millisecond
void RTCTickCallback(void)
{
++counter;	// Increment the 1 ms counter.
if(500 == counter )	// 1/2 second yet ?
{
counter = 0;	// reset the counter so we start over
blink_state ^= 1;	// Use the "C" xor operator to toggle

// write to the LED.
digitalWrite(13,blink_state);
}
}
// Called first to perform and one time initialization
// Interrupts are already enabled.
void setup(void)
{
pinMode(13,OUTPUT);
}
void loop(void)
{
   // No need to do anything here!
}