# API Reference

## Digital I/O
Digital I/O is used to read and write bits and ports. Bits are referenced to by their pin numbers, and must first have their direction set (called their mode, as in pinMode). A port is a group of pins, and current two pre-defined ports are supported, 0 and 1. And enhanced function has been added that allows defining a group of bits as a port. This is very useful as often a complete hardware port is not available due to special functions that may be on a given port.
### pinMode() - Set the direction of a pin.
void pinMode(int pin, int mode)
int pin	Selects which pin
int mode	Set the mode, INPUT or OUTPUT.

The pin refers to a logical pin number which in turn maps to a phsyical pin number. See the Appendix A for pin assignments. This is done to set up an I/O bit, and is required before use. After the mode has been set, digitalRead() and digitalWrite() may be used. Pins set for output may also be read from. Pins set for input will have the pull resistor enabled. See the Appendix for a definition of pins to port bit.

Example:

pinMode(0,OUTPUT);
digitalWrite(0,1);

### pinModeEx() - Advanced pin mode setting for Flexis.

void pinModeEx(int pin, int config)
int pin	Selects which pin
int config	See table

This is only for Flexis parts. Note that mode bit that are not enabled will be reset.

Define	Function
INPUT	Set pin to input
OUTPUT	Set pin to output
HI_DRIVE	When high drive is selected, a pin is capable of sourcing and / sinking greater current. Even though every I/O pin can be selected as high drive, the user must ensure that / the total current source and sink limits for the MCU are not exceeded. Drive strength selection is intended / to affect the DC behavior of I/O pins. However, the AC behavior is also affected. High drive allows a pin / to drive a greater load with the same switching speed as a low drive enabled pin into a smaller load. / Because of this, the EMC emissions may be affected by enabling pins as high drive
SLEW_RATE	Slew control limits the rate at which an output can transition to reduce / EMC emissions. Slew rate control has no effect on pins that are configured as inputs
INPUT_FILTER	Enable a input low pass filter (not available on S08)
PULL_UP	Enable internal pull up. The pull-up device is disabled if the pin is configured as an output

Table 1.1: PinModeEx modes
Example:

pinModeEx(3,OUTPUT | HI_DRIVE | SLEW_RATE); // Set Hi drive and Slew rate
   pinModeEx(3,OUTPUT); // Rest them

### digitalWrite() - Set the state of a pin
void digitalWrite(int pin,int data)
int pin	Selects which pin is affected
int data	0 or 1 (LOW or HIGH)

Outputs the data to the pin specified. Pin must have been set to output using pinMode previously.
 Example:

int led_state = 0;
pinMode(13,OUTPUT);
digitalWrite(13,led_state);

### digitalRead() Read the state of pin
int digitalRead(int pin)
int pin	Selects which pin is read.
Returns:	0 or 1

Returns the state of the pin. The pin must have previously been set to INPUT using pinMode. A pin set to output can also be read, but it well just read back the last value written. Note that pins set to output can still be read back at any time.

Example:

byte switch;
pinMode(3,INPUT);
switch = digitalRead(3);

### portMode() - Initialize an 8 bit port
void portMode(int port, int direction)
int port	Selects which port is affected 0 or 1
int data	INPUT or OUTPUT

Port 0 is pins 0-7 while port 1 is pins 8-15. The port operations allow reading and writing of multiple bits.

portMode(0,OUTPUT);	// bits 0-7 to output
 portWrite(0,0xff);	// Write all 8 bits to 1

### portRead() - Read an 8 bit port
int portRead(int port)
int pin	Selects which port is read.
Returns:	0-255

Reads 8 bits from port 0 or 1.

byte indata;

portMode(1,INPUT);
indata = portRead(1);

### portWrite() - Writes 8 bits to a port.
void portWrite(int port, int value)
int pin	Selects which port 0 or 1
int value	0 - 255

Write 8 bits to port 0 or 1.

portMode(0,OUTPUT);	// bits 0-7 to output
 portWrite(0,0xff);	// Write all 8 bits to 1

### portModeEx() - Initialize a user defined port.
void portModeEx(byte* pins,int direction, int bits)
byte* pins	Address of an array that defines which pins are used for this logical port.
int direction	INPUT or OUTPUT
int bits	How many bits are used.

The user defined array names which pins are in the port. The pins go from LSB to MSB in the array.

Example:

 // Define the “port”
byte my_port[] ={3,4,6,7};	// pin 3 is the LSB, pin 7 is the MSB

portModeEx(&my_port[0],OUTPUT,4); // There are 4 bits in the port.
   portWriteEx(&my_port[0],8,4); // This would set bits 3,4,6 to '0' bit 7 to '1'

### portWriteEx()
void portWriteEx(byte* pins,int data,int bits)
byte* pins	Address of an array that defines which pins are used for this logical port.
int data	Data to be written.
Int bits	How many bits are used.

Write to a user defined port defined by an array of bytes.

 // Define the “port”
byte my_port[] ={3,4,6,7};	// pin 3 is the LSB, pin 7 is the MSB

portModeEx(&my_port[0],OUTPUT,4); // There are 4 bits in the port.
   portWriteEx(&my_port[0],8,4); // This would set bits 3,4,6 to '0' bit 7 to '1'

### portReadEx()
int portReadEx(byte* pins, int bits)
int pins	Address of an array that defines which pins are used for this logical port.
int bit	How many pins are in the array.
Returns:	The value of the port.

## Analog IO
### analogRead() - Input an ADC Channel
int analogRead(int ch)
int ch	Selects which logical channel is read.
Returns:	0 to maximum.

Certain pins are analog input pins, and reading them will return the current value of the voltage on that pin. Note that analog pins can also be used as digital I/O, but if the analogRead call is made any previous pinMode setting will be forgotten and it will be used as an analog input.
By default 10 bits are read, but this can be changed in config.h. 0 is 0 volts and 1023 is 5 volts.

Logical Analog Channel	MCU Function	ADC / CH.
0	PTB0/ADP0	A0
1	PTB1/ADP1	A1
2	PTB2/ADP2	A2
3	PTB3/ADP3	A3
4	PTB4/ADP4	A4
5	PTB5/ADP5	A5
6	PTB6/ADP6	A6
7	PTB7/ADP7	A7
8	PTD0/ADP8/ACMP+	A8
9	PTD1/ADP9/ACMP-	A9
10	PTD3/ADP/10KBIP3	A10
11	PTD4/ADP11	A11
26	Temp Sensor	A26
27	Internal Band Gap	A27

Table 1.2: Analog Channel Assignments

Temp = 25 - ((VTEMP -VTEMP25) / m)

#define POT_PIN 0 // Use channel 0.
int val;
val = analogRead(POT_PIN);

### analogWrite() - PWM output
void analogWrite(int ch,int data)
int pin	Selects which pin is affected
int data	0 to PWM_MAX

Writes to a PWM pin and sets the duty cycle.

Channel	MCU Function	FB32	NANO32	MINI32
0	PTE2 TPM1-CH0	D3	E2	D3
1	PTE3 TPM1-CH1	D4	E1
2	PTF0 TPM1-CH2	D5	F0	D5
3	PTF1 TPM1-CH3	D6	F1	D9
4	PTF2 TPM1-CH4	D7	F2
5	PTF3 TPM1-CH5	D11	F3
6	PTF4 TPM2-CH0	D8	F4	D8
7	PTF5 TPM2-CH1	X		X

Table 1.3: PWM Channels

  // Set PTE2 to 50% duty cycle
analogWrite(0, 512);

## Time functions

### micros() - Return the clock in microseconds
long micros(void)
Returns:	A 32 bit value that is the clock time in microseconds.

The clock is a counter that starts at reset.

long startime = 0;
loop()
{
// something like this is much better that delay!
if(0 == starttime)
starttime = micros();
// Always use >= or you might miss the exact time.
if( (micros() - startime) >= 500 )
{
starttime = micros();
// do what you needed to do every 500 us.
}
}

### millis() - Return the clock in milliseconds
long millis(void)
Returns:	A 32 bit value that is the clock time in milliseconds.

The counter is return in milliseconds.

long startime = 0;
loop()
{
// something like this is much better that delay!
if(0 == starttime)
starttime = millis();
// Always use >= or you might miss the exact time.
// Wait for 500 milliseconds
if( (millis() - startime) >= 500 )
{
starttime = millis();
// do what you needed to do every 500 milliseconds
}
}

### delay() - Delay in milliseconds
void delay(long delay)
long delay	Delay in milliseconds

This does not return until the delay is up, so it will stall the thread. Not advised on interrupt threads.

int ledPin = 13; // LED connected to digital pin 13
// NOTE: This works fine but is not the recommended method.
void setup()
{
  pinMode(ledPin, OUTPUT); // sets the digital pin as output
}

void loop()
{
  digitalWrite(ledPin, HIGH); // sets the LED on
  delay(1000); // waits for a second
  digitalWrite(ledPin, LOW); // sets the LED off
  delay(1000); // waits for a second
}

### delayMicroseconds() - Delay in microseconds
void delayMicroseconds(int delayus)
long delayus	Delay in microseconds

This does not return until the delay is up, so it will stall the thread. Not advised on interrupt threads.

int outPin = 8; // digital pin 8

// NOTE: This works but is not recommended

void setup()
{
  pinMode(outPin, OUTPUT); // sets the digital pin as output
}

void loop()
{
  digitalWrite(outPin, HIGH); // sets the pin on
  delayMicroseconds(50); // pauses for 50 microseconds
  digitalWrite(outPin, LOW); // sets the pin off
  delayMicroseconds(50); // pauses for 50 microseconds
}

### pulseOut() - Generate a pulse stream
void pulseOut(int pin,int frequency,int nPulses)
int pin	Can only be pin 8
int frequency	Frequency in Hertz
int nPulses	How many pulse 0 = infinite.

This function uses TMP2 CH0 to generate frequencies and pulse bursts. This is found on output D8. It can generate frequencies from 1 Hz to about 4.5 MHz, however at higher frequencies repetitive pulse bursts can consume too much overhead as in the counted mode ( ie. NPulses > 0) some interrupt overhead is used.

    // Send 10 1Khz pulse out
    pulseOut(8,1000,10);

### pulseStop() - Stop the pulse stream
void pulseStop(int pin)
int pin	Can only be pin 8

This will shut off the the pulse stream.

     // Start a continuous pulse stream.
     pulseOut(8,1000,0);
     // End it
     pulseStop(8);

### pulseRunning() - Return the remaining pulses
int pulseRunning(int pin)
int pin	Can only be pin 8
Returns:	Number of pulses remaining 0 is infinite.

Returns the number of pulse remaining when a count is given.

   // Send 100 1Khz pulses out
   pulseOut(8,1000,100);

// wait for them to all go out.
while(pulseRunning(8) )
        ;

### pulseIn()
Currently not implemented.

### singleshotPulse() - Send a pulse
void singleshotPulse(int ch, dword time_us)
int ch	Any PWM channel (see chart in analogWrite)
int time_us	Amount of time to send the pulse.

This is an enhancement to the wiring specification. It is intended for driving RC servos, but of course can be used for any application that requires a precision repeatable pulse. Each time it is called it will emit a single pulse of the specified duration. See analogWrite for a table of channels.

   // Send a 1.5 ms pulse on channel 0
singleshotPulse(0, 1500);

## Interrupts
Interrupts can be used to count pulses, measure pulses and signal external events.
### attachInterrupt() - Configure an interrupt
void attachInterrupt(int intno,PFNCALLBACK cb,int mode)
int intno	Interrupt number (see table)
PFNCALLBACK cb	Pointer to callback function
int mode	Mode (see mode table)

Sets up to cause an interrupt on an input event, edges and levels on the pins shown in the table.

Number	Function	Modes	FB32	NANO	MINI
0	PTE2 TPM1-CH0	R,F,C	Pin 3		D3
1	PTE3 TPM1-CH1	R,F,C	Pin 4		D5
2	PTF0 TPM1-CH2	R,F,C	Pin 5
3	PTF1 TPM1-CH3	R,F,C	Pin 9		D9
4	PTF2 TPM1-CH4	R,F,C	Pin 10
5	PTF3 TPM1-CH5	R,F,C	Pin 11
6	PTF4 TPM2-CH0	R,F,C	Pin 8
7	PTF5 TPM2-CH1	R,F,C	Speaker
8	PTG3	H,L,R,F	Pin 2
9	PTG2	H,L,R,F	Pin 4
10	PTG1	H,L,R,F
11	PTG0	H,L,R,F
12	PTD2	H,L,R,F			D4
13	PTD3	H,L,R,F
14	PTB5	H,L,R,F			A2
15	PTB4	H,L,R,F			A1

Table 1.4: Interrupt Channels
LOW	Logic 0
HIGH	Logic 1
CHANGE	Both Edges
RISING	Rising Edge
FALLING	Falling Edge

Table 1.5: Interrupt Modes

// Measure the period of a pulse.
long lastcount=0;
long period;
void interruptCallback(void)
{
long m = micros();
period = m - lastcount;
lastcount = m;
}
void setup(void)
{

// Apply a pulse to pin 3 to test this.
attachInterrupt(0,interruptCallback,RISING);

}
void loop(void)
{
}
Interrupt Example

### detachInterrupt() - Remove interrupt
int detachInterrupt(int intno)
int intno	The same interrupt number that was used in the attach.

Removes the interrupt from the interrupt channel.

### interruptMode() - Change the mode of an interrupt
void interruptMode(int intno,int mode))
int intno	The same interrupt number that was used in the attach.
int mode	See table of interrupt modes.

Modifies the mode of an interrupt that was previously attached to.

### ENTER_CRITSEC() EXIT_CRITSEC() Macros
void ENTER_CRITSEC(void)

ENTER_CRITSEC()/EXIT_CRITSEC() is the preferred method for disabling interrupts when mutual exclusion is required for two reasons:

- It will restore the previous state of the interrupts. So if interrupts had been disabled before a function requiring mutual exclusion the will remain disabled.
- It nests, meaning that the interrupts will not be re-enabled until the outer EXIT_CRITSEC() is executed. If you simply disabled the interrupts and were to call a function that also required mutual exclusion, it would return with interrupts re-enabled an the exclusion would have been lost.

It calls cli() and sti():

volatile byte SR_level = 0x00;
volatile word saved_SR = 0x00;
void CLI(void)
{
   // If this is the first call, the save SR and disable int.
   if (++SR_level == 1)
   {
      asm
      {
       move.w SR,D0;
       move.w D0,saved_SR;
       ori.l #0x700,D0;
       move.w D0,SR;
       }

   }
}

void STI(void)
{
   // If this is the last call, then restore SR.
   if (--SR_level == 0)
   {
      asm
      {
        move.w saved_SR,D0;
        move.w D0,SR;
      }

   }
}

In the following example, vdata can be modified by an interrupt so we need to insure not concurrent access to it when we modify it.

// vdata can be modified in an interrupt.
myfunction(struct* vdata)
{
ENTER_CRITSEC();
if( vdata->flag )
{
vdata->flag = 0;
strcpy(vdata->str,savedata);
}
EXIT_CRITSEC();
}
### interrupts() - Enable MCU interrupts
void interrupts(void)

This enables the MCUs interrupts. See ENTER_CRITSEC().
### noInterrupts() - Disable MCU interrupts
void noInterrupts(void)

Disable the MCU's interrupts. See EXIT_CRITSEC().