# Extension API
## Serial Ports
Both SCI1 and SCI2 (ports 0 and 1) are supportd. Each port you plan to use must first be initialized. The driver is fully interrupt driven, both send and receive and uses 80 byte buffers.
### Serial_Init()
void Serial_Init(int port)
int port	Selects which is initialized. 0 or 1

This initializes the ports and sets the baud rate to 9600 8,1.

Serial_Init(SCI1);

### Serial_setbaudrate()
byte Serial_setbaudrate(int port,byte baud)
int port	Selects which port is affected 0 or 1
int baud	Baud rate selector e.g. BAUD_115200
Return:	0 if no error, BAD_BAUD_RATE if undefined baud rate.

Sets the baud rate for the port.
Available baud rates:
BAUD_1200
BAUD_2400
BAUD_4800
BAUD_9600
BAUD_19200
BAUD_38400
BAUD_57600
BAUD_115200

Table 1.1: Serial Baud Rates

Serial_Init(SCI1);
Serial_setbaudrate(SCI1,BAUD_19200);

### Serial_rxbyte()
byte Serial_rxbyte(int port, byte rxdata)
int port	Selects which port
Byte rxdata	Pointer to data to receive.
Return:	0 if character available, RX_EMPTY if no receive data.

Checks the buffer to see if a character is available. Returns 0 if available and puts the character in to rxdata. Does not wait.

### Serial_txbyte()
byte Serial_txbyte(int port, byte data)
int port	Selects which port
byte data	Pointer to data to receive.
Return:	0 if no error, TX_FULL if tx buffer is full.

Serial Port Example Code

// General form of the calls.
byte rxdata;	// Variable to receive a character.
byte rc;	// return code.
Serial_init(SCI1);	// Must initialize
Serial_setbaudrate(SCI1,BAUD_115200);	// Set the baud rate to 115200
Serial_txbyte(SCI1, 'A');	// Send the character 'A'
rc = Serial_rxbyte(SCI1,&rxdata);	// See if an rx character is there.

// Was there a character waiting?
if(0 == rc )
{
// Yes, so echo it. Loop until there room in buffer.
while(TX_FULL == Serial_txbyte(SCI1, rxdata))
;
}

## I2C

### I2CInit()
void I2CInit(void)
Notes: This call also will un-hang any I2C device. With many I2C devices, if the MCU is reset or crashes while the device is sending, the device will still need to finish sends a byte. / This call manually clocks away this remaining data.

The baud rate is initially set to 100KHz. Different devices can handle higher baud rates depending upon the devices specification, Vdd voltage and length of connection wires.

### I2CSetBaudrate()
byte I2CSetBaudrate(int ratekhz)
int ratekhz	Sets the I2C Bus baud to the approximate value requested
Returns	ERROR_NONE, ERROR_BUSBUSY

You can't set the baud rate while in a transaction.

// Wait until not busy to set the baud rate.
while (I2CSetBaudrate(300) == ERROR_BUSBUSY)
;

### I2CSetDeviceAddress()
void I2CSetDeviceAddress(byte address)
byte port	Set the I2C Device address. Generally from the spec sheet of the device.

### I2CSend()
byte I2CSend(byte* data,word size)
byte data	Pointer to data to send.
word size	How many bytes to send
Return:	ERROR_NONE,ERROR_BUSBUSY

### I2CRecieve()
byte I2CRecieve(byte* data,word size)
byte* data	Pointer to receive buffer.
word size	How many bytes to send
Return:	ERROR_NONE,ERROR_BUSBUSY

### I2CSetDeviceAddress()
void I2CSetDeviceAddress(byte address)
byte port	Sets the I2C Device address. Generally from the spec sheet of the device and the schematic of the board.

Some I2C Devices have address lines that allow modifying the the devices address, so you need to look at both the specification sheet for the device and the schematic of the board.
### I2CGetRemainingSendBytes()
word I2CGetRemainingSendBytes(void)
Returns:	Bytes left to be sent.

This returns how many bytes are left in the I2C send buffer.
### I2CGetRemainingRecieveBytes()
word I2CGetRemainingRecieveBytes(void)
Returns:	Bytes left to be received.

### I2CGetLastError()
byte I2CGetLastError(void)
Returns:	Returns last error

This call helps because certain errors will not be detected when a call is initially made. It is not cleared until read, so it is a good idea to read it before and after a transaction.

ERROR_NONE	No error
ERROR_BUSBUSY	Busy with a current transaction
ERROR_NAK	Did not receive a ACK (normal if device had no more data to send) Could indicate no device or you used to wrong address
ERROR_ARB_LOSS	Another master was detected.

Table 1.2: I2C Errors

// 24C32 I2C EEPROM – 32 byte pages
// Address line A1 high, A0 and A2 low.
#define I2C_EEPROM_ModuleAddress 0xA4 // One of the address set bit is high.

typedef struct _eeprom_write {
word address;
byte data[32];
} EEPROM_WRITE_BLOCK;

EEPROM_WRITE_BLOCK eeprom_write_data;

setup()
{
I2CInit();
I2CSetDeviceAddress(I2C_EEPROM_ModuleAddress);
eeprom_write_data.address = 0;

for( i=0 ; i<32 ; ++i)
eeprom_write_data.data[i] = i;

interrupts();
      I2CSend((byte*) &eeprom_write_data,sizeof(EEPROM_WRITE_BLOCK));
}

## Button

There is a button the Firebird32 connected to PTG0. These APIs use a a callback for each time it changes state. See example at end of section.

### BUTTONInit()

void BUTTONInit(void))
Returns:	Nothing

This initializes the input and sets up the de-bounce timer.

### BUTTONSetCallback()

void BUTTONSetCallback(void(*func)(int state))
func	Pointer to receive buffer.
Return:	Nothing

The state is 0 when the button is pushed.

#define LED	13 // Pin number for the LED

// Our call back function prototype.
void OnButtonChanged(int state);

// This is called each time the button changes state.
// state is the de-bounced state of the button
void OnButtonChanged(int state)
{
// Turn the LED off or on based on the state
// of the button.
if(!state) // If pushed, turn button off
digitalWrite(LED,0);
else
digitalWrite(LED,1);
}

// Initialize for the button and LED.
void setup()
{
BUTTONInit();
BUTTONSetCallback(OnButtonChanged);
      pinMode(LED,OUTPUT);

}

## LCD
If you connect the LCD as follows, it will work with the framework. This is how the LCD is connected on Wytec boards.
This assumes an HD44780 or compatible LCD module, 4 bit interface.

PTA0	RS (data/command) (Pin 4 on LCD module)
PTA1	EN (Write pulse) (Pin 6, also called E)
PTA2	Data 4 (Pin 11)
PTA3	Data 5 (Pin 12)
PTA4	Data 6 (Pin 13)
PTA5	Data 7 (Pin 14)

Table 1.3: LCD Port A Connection

Pins 1 & 5	should be 0V on the LCD module
Pin 5	is R/W and we only use W so ground it
Pin 3	should go to ground thru a 1K resistor
Pin 15	is the positive side of the back light LED and can be connected to +5
Pin 16	is the ground side of the back light LED, and should go to ground thru a 100 OHM or higher resistor. You could also hook up a PWM signal here thru a transistor for variable back light. (note: The resistor can be on either side of the LED. You MUST have a resistor)

Table 1.4: Other LCD Connections on the LCD connector (see devices documentation)

### LCDInit()
void LCDInit(int width)
int width	The width of each line in the LCD.

This initializes the ports and sets the width. Setting the width will allow the code the clear a line first.

### LCDGetWidth()
int LCDGetWidth(void)
Returns:	The width that was set.

### LCDWriteLine()
void LCDWriteLine(char* string, byte line)
char* string	Pointer to data buffer.
byte line	Which line to write it to – up tp 4 lines.

## Keypad
These API's support the Firbird32 standard keypad that connects to J5 on the main board.

The standard keyboard is wired like this to Port D:

MCU PIN	Col. 1 PTD0	Col. 2 PTD1	Col. 3 PTD2	Col. 4 PTD3
Row 1 PTD4	1	2	3	A
Row 2 PTD5	4	5	6	B
Row 3 PTD6	7	8	9	C
Row 4 PTD7	*	0	#	D

Table 1.5: Keyboard Connections

### KPADInit()
void KBRDInit(void)
Returns: Nothing

This should be called before using the keyboard. It initializes port D and sets up a polling routine.

### KPADReadChar()

byte KBRDReadChar(void)
Returns: key if one is waiting or KBRD_NOCHAR

There is no buffer, so the keypad should be polled often.

// Echo the keypad to the LCD.
setup()
{
   LCDInit(8,2);
   KPADInit();
}

void loop(void)
{
  char c;
  static char lcd_msg[8];
  static byte lcd_index = 0;

  // Echo the keypad to the LCD
  // Poll the keypad....
  if(KPAD_NOCHAR != (c = KPADReadChar()))
   {
      LCDClear();
// If there less than 8 chars, then add this one
      if( lcd_index < sizeof(lcd_msg) - 1)
{
        lcd_msg[lcd_index++] = c;
}
      else
      {
 // Start over with a new line.
        lcd_index = 0;
        lcd_msg[lcd_index++] = c;
      }
      lcd_msg[lcd_index] = 0;
      LCDWriteLine(lcd_msg, 0);

    }

}
## Console printf Support
The printf function can be directed to either serial port, the LCD, the debug console or any combination of them. There are various CONFIG.H setting and the device must be initialized.

void SetActiveConsole(int cons);

## Speaker Support
The Firebird32 and Nano32 both have speakers.